## Slide 1
Muon Acceleration for Muon g-2 Experiment at J-PARC
Y. Kondo2, R. Kitamura3, Y. Nakazawa4, Y. Sue5, S. Bae6, H. Choi6, S. Choi6, K. Futatsukawa1, K. Hasegawa2, K. Inami5,T. Iijima5, H. Iinuma4, N. Kawamura1, B. Kim6, H.S. Ko6, Sirui Li3, T. Mibe1, Y. Miyake1, T. Morishita2, G.P. Razuvaev7, N. Saito1, K. Shimomura1, E. Won6, T. Yamazaki1, H. Yasuda3,M. Yotsuzuka5
M. Otani 1
1 KEK
2 JAEA
3 Univ. of Tokyo
4 Ibaraki Univ.
5 Nagoya Univ.
6 SNU
7 BINP

## Slide 2: Contents
Introduction
Muon linac design
Muon acceleration experiment
Prospects
Summary

## Slide 3: Muon Anomalous Magnetic Moment (g-2)
More than 10 years, muon g-2 anomaly has not been solved.
Needs more precise measurement with, if possible, completely different method.
~3σ
Systematic [ppb] | 
B field | 170
Lost muons | 90
CBO | 70
E and pitch | 50
Gain changes | 120
Pileup | 80
BNL E821 (2006)
Standard Model
Related to beam
Low emittance muon beam offers new method.

## Slide 4: Contents
3GeV proton
Neutron target
400MeV linac
3GeV RCS
MLF
Muon target
Experimental site J-PARC MLF Materials and Life science Facility

## Slide 5: Contents
J-PARC MLF Materials and Life science Facility
H-line

## Slide 6
Production target
(20 mm)
3 GeV proton beam
( 333 uA)
Surface muon beam
(28 MeV/c)
Muonium Production
(300 K ~ 25 meV⇒2.3 keV/c)
Muon g-2/EDM Experiment at
J-PARC with Ultra-Cold Muon Beam
Surface muon
Ultra Cold m+ Source
Muon LINAC (300 MeV/c)
Muon
storage
Silicon
Tracker
66 cm
Super Precision Storage Magnet
(3T, ~1ppm local precision)
Features:
No strong focusing
Super-low emittance muon beam
Compact storage ring
Full tracking detector
Completely different from BNL/FNAL method

## Slide 7: Muon linac
Utilize resources and experiences at J-PARC H- linac and KEK
  324 MHz RFQ
  1.3 GHz high power klystron
Low current and duty
  IH-DTL with alternative phase focusing.
~40m
40 MeV
β=0.7
USμ
RFQ
IH-DTL
DAW CCL
Disk-loaded (DL)
212 MeV
β=0.9
3.2 m
0.3 MeV
β=0.08
5.6 keV
β=0.01
324 MHz
1296 MHz
4.5 MeV
β=0.3
1.4 m
16 m
15 m
Energy [MeV] | 212
Intensity [/s] | 
Repetition [Hz] | 25
Pulse length [nsec] | 10
Normalized εt [π mm mrad] | 1.5
Δp [%] | 0.1
Energy [MeV] | 212
Intensity [/s] | 
Repetition [Hz] | 25
Pulse length [nsec] | 10
Normalized εt [π mm mrad] | 1.5
Δp [%] | 0.1

## Slide 8: RFQ
f [MHz] |  | 324
Length [m] |  | 3.2
Energy [keV] | In | 5.6
 | Out | 340
Inter-vane V [kV] |  | 9.3
Power [kW] |  | 4.2
J-PARC H- spare is used.
  Inter-vane voltage is scaled by mass
Simulation shows good transmission to muon.
Δx (cm)
Δy (cm)
ΔΦ (deg)
ΔE (MeV)
Cell#
Good transmission (95%).

## Slide 9: IH-DTL
Interdigital H-mode DTL
  TE11 mode and π mode acceleration
Alternative phase focusing
Transverse: defocus longitudinal: focus
focus defocus
f [MHz] |  | 324
Length [m] |  | 1.3
Energy [MeV] & β | In | 0.34 (0.08)
 | Out | 4.5 (0.28)
# of cells |  | 16
Φs [deg.] |  | -44 ~ 48
Finish design and fabricate proto-type [M. Otani et al., Phys.Rev.AB 19, 040101, 2016]

## Slide 10: DAW-CCL
f [MHz] | 1296
Length [m] | 16
Output Energy[MeV] | 40 MeV (β=0.7)
# of cells | 16
Φs [deg.] | -30
Power [MW] | 4.5
Disk and Washer Coupled Cell Linac
  Simple structure and high coupling
Finish cavity and dynamics design

## Slide 11: DLS
f [MHz] |  | 1296
Energy [MeV] | In | 40
 | Out | 212
E0 [MV/m] |  | 20
Φs [deg.] |  | -10
# modules |  | 4
Disk-loaded travelling wave structure.
  High-gradient acceleration.
  Due to β≠1, synchronized β cell design is conducted.
Finish reference design [Y. Kondo et al., J. Phys. :Conf. Ser. 875, 012054 (2017).]

## Slide 12: Design Summary
Momentum spread
Δpdesign = 0.1%
Emittance evolution
Satisfy the requirement.
 | Init. | RFQ | IH | DAW | DLS
Decay survival [%] | 83 | 81 | 98 | 96 | 99
Transmission [%] | 87 | 95 | 99.9 | 99.5 | 99.9

## Slide 13: Contents
J-PARC MLF Materials and Life science Facility
Muon Acceleration Experiment @ D-line
H-line

## Slide 14: Muon Cooling for Acceleration Experiment
First observation in late 1980’s [Phys.Rev.A, 39, 6109]
μ+ (~3 MeV)
μ+
Mu (μ+ e-)
Mu- (μ+ e- e-)
Acceleration after cooling by Mu- generation
Easy & cheaper cooling method

## Slide 15: History for the Experiment
2014
2015
2016
2017
Transportation (2014/8)
assmbly@J-PARC (~2015/5)
slow μ+ &BPM test (2016/2)
Mu- observation (2016/12)
slow μ+ profile (2017/3)
acceleration test (2017/10)
Lead by RIKEN-RAL group

## Slide 16: Observation of Mu-
Al foil(Mu-generation)
Electric deflector
Electric quadrupole
Magnetic bend
detector
μ+ (~3MeV)
Dec. 2016@MLF
Result
signal region

## Slide 17: RFQ Acceleration Setup
@J-PARC MLF test muon beamline(D2)
μ+ (~3MeV)
Mu- generation (3 MeV→<keV)
Electro-static (5 keV)
RFQ (90 keV)
Diagnostic beamline
(Q-pair and bending magnet)
MCP detector
4.3 m
2 m
 | H- | μ
Injection (keV) | 50 | 5.6
Extraction | 810 | 89
IntervaneV(kV) | 81 | 9.1
Power (kW) | 180 | 2.3

## Slide 18
18
μ+ (~3MeV)
5.6 keV
90 keV
Mu- production
RFQ
Diagnostic beamline
MCP
Acceleration test (Oct. 24th – 30th ,2017)

## Slide 19: Result
World first muon acceleration [ S. Bae et al., Phys. Rev. AB 21, 050101, 2018. ]

## Slide 20
20
Acceleration this year (Nov. 2nd – 8th)
Muon bunch measurement with buncher and new detectors

## Slide 21: Some plots
Expected
Data in Nov.
Will be released by Y. Sue (Nagoya Univ.) soon.
Stay tuned!
By Y. Sue (Nagoya Univ.)
Notes: カプラ、セラミックにTiNコーティング、初めはでる

## Slide 22: Prospect
Acceleration with RFQ and IH @ H-line
μ
g-2
MuSEUM DeeMe
MuSEUM DeeMe
μ+ (~4 MeV)
Mu- generation
RFQ
IH-DTL
Detector
OK
OK
OK
design
~4 MeV
M. Otani et al., Phys. Rev. AB, 19, 040101, 2016.

## Slide 23: H-line Status
Beamline components are almost ready.
Electric sub-station is being constructed.
Will be ready in the end of next fiscal year.

## Slide 24: Summary
Basic design of the muon linac completed.
We succeeded in accelerating muon using rf accelerator for the first.
H-line is getting ready for accelerating more muons.
This work was supported by JSPS KAKENHI Grant Numbers JP15H03666, JP16H03987, JP18H03707.