## Slide 1: The Focusing DIRC Prototype
N. Arnauda, M. Borsatoa,, B. Deyb, D.W.G.S. Leithc, K. Nishimurae, B.N. Ratcliffc, Doug Robertsd, G. Varnere, J. Va’vrac
aLaboratoire de l’Accélérateur Linéaire, IN2P3/CNRS & Université Paris Sud, France bUniversity of California, Riverside, USA cSLAC, Stanford University, USA dUniversity of Maryland, USA eUniversity of Hawaii, USA

## Slide 2: The Focusing DIRC
Based on the BaBar DIRC detector
To deal with higher luminosity (~x100), several changes:
  New Optical Camera
    25 times smaller
    Radiation-resistant fused silica
  New PMT readout
    Hamamatsu H8500
    10 times faster than BaBar PMTs
    Highly pixelated
  Would have been main PID detector of the SuperB experiment
BaBar DIRC

## Slide 3: FDIRC Photon Camera
Cherenkov angle is determined by x-y pixel location
Time is used to:
  Reduce background
  Do chromatic corrections
New wedge glued to existing bar box window
Cylindrical mirror
  Removes bar thickness contribution to resolution in y-direction
Double-folded mirror optics
  Provides easy access to detectors

## Slide 4: Compact Focusing Optics

## Slide 5: Photon Detection
Photo-detectors
  12 Hamamatsu H8500 MaPMTs placed in the region most hit by cosmic rays
    48 needed for complete coverage of FBLOCK
  MaPMTs have 64 channels each
    6mm x 6mm pixels
  Transit Time Spread ~140ps
Electronics
  SLAC amplifiers with x40 gain
  IRS-2 waveform digitizing electronics (Hawaii & SLAC)
    2.7 GHz sampling rate
    Analog storage depth up to 12 μs (ring buffer)
    On-ASIC Wilkinson ADC for digitization
    Digitized waveforms analyzed offline
Instrumented PMT Plane

## Slide 6: Building the FDIRC Prototype
Optical coupling between bar box window and new Wedge is 50-75 mm-thick Epotek 301-2 epoxy.
Measuring FBLOCK:
FBLOCK placed into Fbox:
New Wedge glued to bar box:
Bar box with the new Wedge:

## Slide 7: Cosmic Ray Telescope Facility at SLAC

## Slide 8: Prototype in CRT
σtrack ~ 1.5 mrads track resolution
σx-y tracking ~ 5-6 mm
σstart time < 90 ps
Emuon > 1.6 GeV muon energy lower limit
3D tracking (very important !!)
46”- thick iron absorber, 55” x 90” x-y size
FDIRC prototype located in CRT:
SLAC Cosmic Ray Telescope (CRT):
Fbox
Bar box
SLAC-PUB-13873 (2010)
Detector plane

## Slide 9: Data Collection
About 600k cosmic triggers recorded in SLAC CRT
Laser light sent inside FBLOCK after each trigger, with suitable time delay, for calibration
Shorter run taken with in-time laser light to simulate random background
GEANT4 simulation includes the CRT in addition to the FDIRC prototype

## Slide 10: Reconstruction Overview
The goal is to determine the angle that a given photon measured in the FDIRC makes with respect to a track
If we call the track direction vector p and the photon direction at the point of creation k, then:
Tracking system measures p, FDIRC measures k.
FDIRC needs to translate a hit in a PMT pixel into a k-vector

## Slide 11: Bar Ambiguities
As the photon propagates through the bar its direction changes w.r.t. its original direction:
  Each bounce in the horizontal direction changes the sign of kx
  Similar for vertical bounces and ky
  And backward-going photons that hit the end mirror change sign of kz
This creates a potential 8-fold ambiguity between the photon’s generated direction and it’s direction as it leaves a quartz bar
We make no attempt to actually calculate the number of bounces so we treat these ambiguities as possible solutions
In reality, timing will resolve the z-ambiguity and some of the ambiguities will give rise to non-physical values of the Cherenkov angle.

## Slide 12: More Ambiguities
After a photon leaves a quartz bar, it propagates through wedges and the FBLOCK before being detected by the PMT.
Reflections off the surfaces of the wedges and sides of the FBLOCK can lead to further ambiguities
  There is more than one path, with different k, that can bring a photon from a quartz bar to a given pixel

## Slide 13: Photon Dictionary
Possible k solutions from a given pixel are determined via a dictionary compiled from single photon simulations
Fixed wavelength, generated isotropically
For each pixel/bar combination, store kx, ky and t for photons
Multivalued due to multiple paths

## Slide 14: Time of Propagation
Primary variable used to reject background and resolve ambiguities is measured Time of Propagation – expected Time of Propagation:
dTOP can also be used to correct for chromatic dispersion

## Slide 15: Time Calibration
Pixel-by-pixel time calibration done by injecting laser pulses after every cosmic trigger.
Monte Carlo simulation used to decouple geometric effects from electronics effects

## Slide 16: dTOP: Data vs. Monte Carlo
Data
Monte Carlo
Monte Carlo dTOP distribution is closer to data after adding a time resolution smearing of ~600ps. (derived from laser calibration)
Work is in progress to improve timing resolution.
Forward Photons
σ ~ 750 ps
σ ~ 716 ps
ns
ns

## Slide 17: dTOP: Data vs. Monte Carlo
Data
Monte Carlo
Monte Carlo dTOP distribution is closer to data after adding a time resolution smearing of ~600ps. (derived from laser calibration)
Work is in progress to improve timing resolution.
Backward Photons
σ ~ 1.13 ns
σ ~ 1.2 ns
ns
ns

## Slide 18: Cherenkov Angle Resolution
σ ~ 10.4 mrad
All angles
|dTOPforw| < 2ns
|dTOPbackw| < 2.5ns
The measured Cherenkov angle resolution (10.4 mrads) is somewhat worse than MC resolution (9.1 mrads) presently.
Cherenkov angle [mrad]

## Slide 19: Chromatic Dispersion
Color of dots correlated with photon wavelength

## Slide 20: dTOP/Lpath vs. ΔθC Data vs. MC
dTOP/Lpath = (TOPmeasured - TOPexpected)/Lpath
dTOP/Lpath = (TOPmeasured - TOPexpected)/Lpath
Δθc [mrads]
Δθc [mrads]
Use this correlation from datato correct θc by time. In forward direction it is less effective.
Forward Photons
Backward Photons

## Slide 21: Cherenkov Angle Resolution: Chromatic Correction
We gain about ~0.8 mrads. MC resolution is slightly better. It gains ~ 1 mrads.
Cherenkov angle [mrad]
Cherenkov angle [mrad]
Cherenkov angle [mrad]
Cherenkov angle [mrad]
Data
All angles
No chromatic correction
MC
All angles
No chromatic correction
MC
All angles
With Chromatic Correction
Data
All angles
With Chromatic Correction
σ ~ 8.9 mrad
σ ~ 7.9 mrad
σ ~ 10.9 mrad
σ ~ 10.0 mrad
Backward Photons Only

## Slide 22: Add Background
Background level: ~250 MHz / bar box, i.e. ~3x what Belle-II TOP counter expects
One can still reconstruct the Cherenkov angle. With better dTOP resolution we may restore the S/N ratio.
Our goal for timing cut is |dTOP| < 1 ns
Background run
All angles
|dTOPforw| < 2ns
|dTOPbackw| < 2.5ns
Nominal run
All angles
|dTOPforw| < 2ns
|dTOPbackw| < 2.5ns
σ ~ 10.4 mrad
σ ~ 10.1 mrad
TDC [ns]
TDC [ns]
Cherenkov angle [mrad]
Cherenkov angle [mrad]
Nominal run - cosmic region of TDC:
Background run - cosmic region of TDC

## Slide 23: Conclusions
Construction of the Focusing DIRC prototype has been successful
600k cosmic triggers taken in the SLAC Cosmic Ray Telescope
Results show that design is working
Still working on improving timing calibration
Chromatic correction is working
Detector appears to be robust against high background levels