## Slide 1: TORCH
Maarten van Dijk On behalf of the TORCH collaboration (CERN, University of Oxford, University of Bristol)
A Cherenkov based Time of Flight detector

## Slide 2: TORCH - motivation
The Timing Of internally Reflected Cherenkov light (TORCH) is an ERC funded R&D project ultimately aiming to deliver a prototype
Particularly well suited for LHCb – most key parameters have been tailored to this context
Particle identification is crucial for LHCb physics
Proposed location of TORCH: in front of RICH2

## Slide 3: Goals
Particle ID is achieved in TORCH through measuring time of flight (TOF) of charged particles
Goal
  To provide 3σ K-π separation for momentum range 2-10 GeV/c (up to kaon threshold of RICH1)
Requirement
  TOF difference between K-π is 37.5ps at 10 GeV/c at 9.5m
  Required per-track time resolution set at 10-15ps
Time of flight difference of pions vs kaons plotted against momentum
Theoretical K-π separation (Nσ) for TORCH as a function of momentum

## Slide 4: Conceptual design
Quartz radiator plate (1cm thick)
Compared to gas-filled RICH:
    High photon yield
    Large chromatic dispersion
Light extracted through total internal reflection to top and bottom of plate
Calculate start time (t0) combined for tracks from same primary vertex
    Adds negligible uncertainty (~few ps)
Timing of Cherenkov photons used to calculate time of arrival of signal track at plate

## Slide 5: TORCH in LHCb
Radiator
Detector
Detector information needs to be associated with track information
High multiplicity of tracks
Tracks are separated in both time and space – essential for pattern recognition
Event
K

## Slide 6: Modular design
Plane of 5 x 6 m2 is needed in LHCb
Single plane is unrealistic
Modular design
    18 identical modules
    250 x 66 x 1 cm3
    Width of modules is a free parameter
Optimization in progress
Without dispersion or
reflection off lower edge
Including dispersion and reflection off lower edge
Module considered
Radiator
Detector
Detector
Detector
Detector plane and radiator for several situations.

## Slide 7: Dispersion
Photon angle relative to track determined by refractive index
Quartz has fairly wide range of refractive index
Reconstructed Cherenkov angle is used to correct for dispersion
~900 photons generated (before QE)
Low limit at 200nm (6eV) due to spectral cut-off due to radiator
~900 photons total

## Slide 8: Simulation
Geant 4
  Simulation software framework
  Currently standalone program
  Data exported to ROOT for analysis
Idealised quartz plate and focusing block
Idealised detector plane
  All photons that hit the detector plane are recorded
Losses due to scattering clearly visible
Viewpoint angles: θ=270° φ=0°
Event display for a single 10 GeV K+ crossing
Raytracing simulation of focusing block

## Slide 9: Simulation
Cherenkov ring segment shows as hyperbola (1000 events)
Primary particles interact with medium
Extra background photons observed from secondary particles
    Secondary particles are 98% electrons
    Photon yield increases by 9%
    Number of photons at detector plane increases by 4%
Noticeable increase in observed photons
Correlated in horizontal but not in vertical (angular) direction
Simulation studies ongoing
Accumulated photons for a thousand 10 GeV K+ crossing the plate 1m under the detector

## Slide 10: Photon loss
Radiator – Amorphous fused silica
Photon loss in radiator
    Rayleigh scattering (~95%)
    Rough surface (σ=0.5nm) (~90%)
    Mirror in focusing block (~88%)
Photon loss in detector
    Quantum efficiency (~20%)
    Collection efficiency (~65%)
    Detector entrance window (cutoff)
Idealised performance
Expected yield: >30 photons
    Single photon time resolution 70 ps
Reflectivity of Suprasil (quartz) coated with aluminium
Quantum Efficiency measured with Photek MCP-PMT. More information can be found on the poster by T. Gys.
Reflectivity as a function of wavelength, shown for several values of surface roughness
Wavelength (nm)
Reflectivity
Wavelength (nm)
Reflectivity (%)
Suprasil – Aluminium
Aluminium – Suprasil
Aluminium – theoretical
CERN PH-DT-DD group

## Slide 11: Photon Detectors
Micro Channel Plate PMT
Leading detector for time-resolved photon counting
Anode pad structure of 8x128 pixels required to achieve 1 mrad resolution on photon angle
  Highest granularity commercially available is the Photonis Planacon: 32x32 pixels
    Not ideal for TORCH because of coarse granularity
Tube under development at industrial partner (Photek Ltd, UK)
Schematic layout of MCP-PMT. Charge footprint shown enlarged.
Schematic layout of the pixellation of the TORCH MCP-PMT [3].

## Slide 12: TORCH R&D
Experimental program at Photek
    Phase 1 – Long life demonstrator
    Phase 2 – High granularity multi-anode demonstrator
    Phase 3 – Square tube with required granularity and lifetime
Technical aims
    Lifetime of 5C/cm2 accumulated anode charge or better
    Multi-anode readout of 8x128 pixels
    Close packing on two opposing sides, fill factor >88%
Development progressing well
    Four long-lifetime demonstration tubes delivered (single channel)
    Lifetime and time resolution tests currently underway
See poster for more information
    J. Milnes & T. Conneely (Photek Ltd.)
Detector
Anisotropic Conductive Film
PCB
Lifetime test showing relative gain as a function of collected anode charge. Cathode efficiency stabilizes. Courtesy of Photek Ltd. [4]
Schematic of detector layout.
Coated (improved) MCP-PMT
Uncoated MCP-PMT

## Slide 13: Time resolution
Per-track resolution of 10-15 ps required
Single photon detector resolution of ~50ps required
    Significant improvement from Photek MCP-PMT’s already observed (single channel tube)
    Challenge will be to maintain resolution for large system
Smearing of photon propagation time due to detector granularity ~50ps
Single photon time resolution of 70 ps achievable
See posters on TORCH MCP-PMT’s for more information
    T. Gys (CERN)
σt = 55ps
Time spread due to pixellation effects of detector.
Experimental measurement of time resolution of Photek MCP-PMT (single channel).
σt = 23ps

## Slide 14: Electronics
Current tests using 8 channel NINO boards
    Low signal (100fC)
    Excellent time resolution (<25ps jitter on leading edge)
    Coupled to HPTDC
Provides time over threshold information
Board for R&D currently in development
  Final readout planned to be done with 32 channel NINO
NINO chips

## Slide 15: Expected performance
PID probabilities for particles identified as pions at L=2x1032 and 2x1033 cm-2 s-1
PID probabilities for particles identified as kaons at L=2x1032 and 2x1033 cm-2 s-1
Correct ID
Wrong ID
Correct ID
Wrong ID
Calculated with simplified TORCH simulation using LHCb events
Coupling to Geant simulation in progress

## Slide 16: Reuse of BaBar DIRC
BaBar DIRC quartz bars may be available for re-use following SuperB cancellation
12 bar-boxes with 12 quartz bars each (1.7x3.5x490cm3)
Length and area almost ideally match TORCH requirements
Suitable adaptation of TORCH optics required
Initial studies indicate suitability for application in TORCH
Studies ongoing
Close-up of lenses
Possible adaptation of the TORCH optics to implement the BaBar DIRC boxes.
Lens design inspired by studies from PANDA DIRC.
BaBar DIRC quartz bars during production
BaBar DIRC

## Slide 17: Conclusions
TORCH is a novel concept to achieve high precision Time-Of-Flight over large area for particle identification using Cherenkov light
Proposed for the LHCb upgrade to complement current particle ID provided by the RICH system, specifically at 2-10 GeV/c momentum
Target resolution for single photons (<70ps) to give required per-track time resolution of 10-15ps for 3σ pion-kaon separation up to 10 GeV/c
R&D programme currently ongoing
    Long lifetime tubes have been delivered and are currently undergoing testing
    Design of next phase is going according to plan
Proposal for reuse of BaBar DIRC quartz bars in preparation

## Slide 18: References
F. Anghinolfi, P. Jarron, F. Krummenacher, E. Usenko, M. C. S. Williams, “NINO: An Ultrafast Low-Power Front-End Ampliﬁer Discriminator for the Time-of-Flight Detector in the ALICE Experiment”, IEEE Transactions on Nuclear Science, Vol. 52, No. 5, October 2004.
M.J. Charles, R. Forty, “TORCH: Time of flight identification with Cherenkov radiation”, Nuclear Instruments and Methods in Research A 639 (2011) 173-176.
The LHCb Collaboration, “Letter of Intent for the LHCb Upgrade”, CERN-LHCC-2011-001, 29 March 2011 (v2).
T. M. Conneely, J. S. Milnes, J. Howorth, “Extended lifetime MCP-PMTs: Characterisation and lifetime measurements of ALD coated microchannel plates, in a sealed photomultiplier tube”, Nuclear Instruments and Methods in Physics Research A 732 (2013) 388-391, http://dx.doi.org/10.1016/j.nima.2013.07.023
R. Forty, “The TORCH project: a proposed detector for precision time-of-flight over large areas”, DIRC 2013, 4 September 2013, Giessen, Germany.
J. Milnes, “The TORCH PMT: A close packing, multi-anode, long life MCP-PMT for Cherenkov applications”, DIRC 2013, 4 September 2013, Giessen, Germany.
R. Gao, “Development of Precision Time-Of-Flight Electronics for LHCb TORCH”, TWEPP 2013, 23-27 September 2013, Perugia, Italy
J. Schwiening, “The PANDA Barrel DIRC”, DIRC 2013, 5 September 2013, Giessen, Germany.
L. Castillo García, “Timing performance of a MCP photon detector read out with multi-channel electronics for the TORCH system”, 14th ICATPP Conference, 25 September 2013, Villa Olmo, Italy.
N. Harnew, “TORCH: A large-area detector for precision time-of-flight measurements”, Fast Timing Workshop, 19-23 November 2013, Erice, Italy.
The TORCH project is funded by an ERC Advanced Grant under the Seventh Framework Programme (FP7), code ERC-2011-ADG proposal 299175.

## Slide 19: Backup slides

## Slide 20: Time / spatial information
Detector measures time of arrival of photons, as well as their relative angles qx, qz
Photons with larger angles take longer to propagate along the bar
Tracks are separated in time and space

## Slide 21: Measuring start time
To determine the time-of-flight, start time (t0) is needed
This might be achieved using timing information from the accelerator, but bunches are long (~ 20 cm)
  So must correct for vertex position
Alternatively use other tracks in the event, from the primary vertex
  Most of them are pions
  Reconstruction logic can be reversed
  Start time is determined from their average assuming they are all pions (outliers from other particles removed)
Can achieve few-ps resolution on t0
Example from PV of same event
After removing outliers