## Slide 1: Side Rail Sag Measurement
T. Hayakawa, K. Inami, K. Suzuki (Nagoya) and T. Kohriki (KEK)

## Slide 2: Purpose (1)
A large sag was observed at the panel-enclosure joint of the Prototype-IV.
  Observed by Inami-san and Hayakawa-san, during the mechanical inspection on the Module01.
    ~0.1 mm sag for 10 kg weight.
    ~0.5 mm rise at the bwd end of the enclosure without rising the Honeycomb panel part.
  It would damage a detector module during its installation to the Belle spectrometer.
    After mounting to the ECL flanges and before connecting to the adjacent modules using z-beams.
    The shear force at the panel-enclosure joint would be ~40% of its total weight.
    Total module weight is ~100 kg including a Strong Back.

## Slide 3: Purpose (2)
A large sag was observed at the panel-enclosure joint of the Prototype-IV. (cont’d)
  Extension of a Strong Back to the enclosure part is being considered to solve this problem.
A question was raised if side rails can really sag that much.
  Side rails should be very rigid in vertical direction.
A measurement has carried out to answer the question.

## Slide 4: Set-up (1)
265 mm
6 Al frames were used to apply distributed load.
20 kg x 4 at the granite table edge.
1450 mm
750 mm
1410 mm
700 mm
Dial gauges on the side rails at around the bwd end.
10 kg x 2 at the fwd end.
8 kg x 2 on the center “end-plate” and side rails.
Emulating a cantilever beam with a distributed load in the enclosure region of the side rails.
  Based on Jim’s suggestion using the side rails for Module02.
Side rails are connected with 5 end-plates at the fwd end, ~1/4, ~1/2, ~3/4 and bwd end to prevent from unwanted bending of the rails, e.g. twisting.

## Slide 5: Set-up (2)
Sag for a given load was measured using dial gauges.
  Lead blocks (11.5 kg/block) were used as load.
    Measured loads: 0, 1, 2, 3 and 4 blocks.
  6 Al frames (3.75 kg in total) were used to distribute the load over the enclosure region.
3.75 kg
26.75 kg
38.25 kg

## Slide 6: Results (1)
Data agree with the concentrated load case unexpectedly.
  Square shape seems better.
Dial gauges were zero-adjusted with Al frame weight.
  Need corrections.
Distributed load
Max. sag = Wl3/(8EI)
B. Concentrated load
Max. sag = Wl3/(3EI)
1. Square shape
I = bh3/12,
where b= 6 mm, h= 45.6 mm.
2. C-shape
I = [ad3 – h3(a-t)]/12,
where a= 7.5 mm, t= 6 mm,
d= 45.6 mm, h= 27.6 mm.
Approx. cross-section
Chart: Load [kgf]
| 0.0 | 1.875 | 7.625 | 13.375 | 19.125 | 24.875
B1 | 0 | 0.034069 | 0.13855 | 0.24302 | 0.3475 | 0.45198
B2 | 0 | 0.028519 | 0.11598 | 0.20343 | 0.29089 | 0.37835
A1 | 0 | 0.012776 | 0.051955 | 0.091134 | 0.13031 | 0.16949
A2 | 0 | 0.010695 | 0.043491 | 0.076288 | 0.10908 | 0.14188
pX | 0 | 0.08 | 0.19 | 0.31 | 0.44
mX | 0 | 0.1 | 0.21 | 0.32 | 0.44
l= 265 mm, E(Al)= 7199.2 kgf/mm2.

## Slide 7: Results (2)
Chart: Load [kgf]
| 0.0 | 1.875 | 7.625 | 13.375 | 19.125 | 24.875
B1 | 0 | 0.034069 | 0.13855 | 0.24302 | 0.3475 | 0.45198
B2 | 0 | 0.028519 | 0.11598 | 0.20343 | 0.29089 | 0.37835
pXcorr | 0 | 0.034 | 0.114 | 0.224 | 0.344 | 0.474
mXcorr | 0 | 0.034 | 0.134 | 0.244 | 0.354 | 0.474
Chart: Load [kgf]
| 0.0 | 1.875 | 7.625 | 13.375 | 19.125 | 24.875
ΔpXcorr | 0 | -6.875e-05 | -0.024546 | -0.019024 | -0.0035013 | 0.022021
ΔmXcorr | 0 | -6.875e-05 | -0.0045462 | 0.00097625 | 0.0064988 | 0.022021
Corrected the data by adding the expected sag of B1 for the Al frame weight (3.75 kg) .
  Measurement agrees with the concentrated load expectation for the square shape cross-section within ±0.025 mm.
  The reason not to agree with the distributed load expectation is unknown.
Extension of the strong back is necessary.
  40 % of the module+SB weight (~100 kg) would bend the side rail by 0.73 mm.