## Slide 1
Matthias Hoek
on behalf of the PANDA Cherenkov Group
The PANDA Barrel DIRC
RICH 2013 | 02.-06. December 2013 | Hayama, Kanagawa, Japan

## Slide 2
FAIR & PANDA Experiment
Barrel DIRC Design
Pattern Reconstruction
Technical Challenges
Prototyping
Conclusions
Overview

## Slide 3
Facility for Antiproton and Ion Research (FAIR)
GSI
Secondary beams
  Broad range of radioactive beams up to 1.5 – 2 GeV/u
  Antiprotons 3 – 30 GeV
HESR
PANDA
5·1010 antiprotons
• 1.5 to 15 GeV/c
High luminosity mode Dp/p ≈ 10-4 with stochastic cooling L = 21032 cm-2s-1
High precision mode (<8.9 GeV/c) Dp/p ≈ 10-5 with electron cooling L = 1031 cm-2s-1
Primary beams
  Heavy Ion Beams
  30 GeV protons (2·1013 s-1)
See CBM presentations
C. Pauly, Mon, 17:25
S. Lebedev, Thur, 18:05
T. Mahmoud, Poster
J. Kopfer, Poster
Notes: Link to CBM talks?

## Slide 4
Physics Goals of PANDA
Precision Hadron Spectroscopy
Exotic States
(Glueballs, Hybrids)
In-Medium Modifications
Nucleon Structure
Hypernuclei
Non-perturbative QCD
Excellent PID required
Notes: Some physics book results
General PANDA physics goals (Map?)
Final states for some key channels

## Slide 5
MVD & Central tracker
dE/dx (<1 GeV/c)
Time-of-Flight
Cherenkov detectors
Barrel & Endcap DIRC
EM-Calorimeter
e-identification
Muon detector
PANDA Detector
Target Spectrometer
Forward Spectrometer
Beam
Target
Solenoid
Yoke + Muon Detector
Central Tracker
20 MHz avg interaction rate
Trigger-less DAQ
Target Spectrometer
  acceptance 5˚ <  < 140˚
  2 T super-conducting solenoid
EMC
MVD
PID system
  Momentum range
  200 MeV/c – 10 GeV/c
Notes: Introduction of PANDA detector

## Slide 6
PANDA DIRC Detectors
EMC
GEM
Endcap DIRC
(5˚-22˚)
Barrel DIRC
(22˚-140˚)
Target Spectrometer
Beam
DIRC Principle
Notes: Picture of TS + geometrical acceptance

## Slide 7
PANDA DIRC Detectors
Barrel DIRC
PID Goal: 3s p/K separation up to 3.5 GeV/c
Endcap DIRC
Novel design
PID Goal: 3s p/K separation up to 4 GeV/c
Kaon distribution of the radiative decay J/y → K+K- g
O. Merle, Development of an Endcap DIRC for PANDA, Mon, 17:00
p/K Cherenkov angle difference at 3.5 GeV/c in fused silica ~8.5 mrad
Notes: Picture of TS + geometrical acceptance
This radiative decay is a benchmark channel for glue balls;

## Slide 8
Evolution of Barrel DIRC Design
Initial Design
Scaled version of BABAR DIRC
250 cm
96 narrow fused silica bars
~ 7,000 PMTs
Expansion volume: water tank
100 cm
Fast Simulation
Next Iteration
Benefit from
SLAC fDIRC R&D
new MCP-PMT advances
place small expansion volume inside yoke
Fused silica bar
requires focusing to achieve required PID performance
bar size dominates resolution
2% mis-ID
98% kaon eff
Notes: fast timing, small pixels, possible chromatic correction
Air gap between lens and bar/expansion volume causes massive
photon loss - only 2-5 photons per track around 90º polar angle
Timing for plate <1ns required (Marko Zuehlsdorf)

## Slide 9
Barrel DIRC Base Design
250 cm
100 cm
Radiator bars (80 pcs)
17mm32mm2400mm
Syn. fused silica
Photon detection
& Electronics
15,000 channels
MCP-PMTs
Fast TDC + ADC FEE
Focussing optics
High-refractive index lens
50 cm
Expansion Volume
Mineral oil
Performance Goals
qc single photon resolution 8-10 mrad
20 detected photons per track (b=1)
Timing resolution ~100 ps
N-LaK 33
Fused Silica
Simulated hit pattern
Notes: General design + numbers
15k readout channels
Timing
Rates

## Slide 10
Barrel DIRC Design Options
Narrow bars with Prism
Plate with Prism
One fused silica prism per sector (5 bars)
Higher photon yield than oil tank design
More ambiguities in reconstruction
Fused silica prism
1 plate per sector (16 cm)
Similar to Belle II iTOP
Less surfaces
Makes best use of timing resolution
Simulated
X-Y hit pattern
30 cm
Notes: Bars or plates

## Slide 11
Barrel DIRC Pattern Reconstruction (Bar)
Use BaBar-like reconstruction approach
Generate Look-up table
The ambiguity background is spread around the true peak
Photon arrival time information is used to reduce the ambiguity background
Reconstructed
Cherenkov angle
for 50 tracks
(with time cut)
Notes: NLAK33 compound lens used in simulation

## Slide 12
Approach inspired by BELLE II
Use photon hit time per pixel & generate PDFs (created from simulation, analytical calculations being developed)
Barrel DIRC Time-Based Likelihood Method (Plate)
1 GeV/c Pion
1 GeV/c Kaon
p+
K+
3.5 GeV/c, 22˚
X-Y
X-T
T-Y
p/K separation at 3.5 GeV/c possible even w/o focussing
R. Dzhygadlo, Simulation and Reconstruction of the PANDA Barrel DIRC, Poster
Notes: T-Y plots are log-scale!
4 sigma resolution achieved
Move from MC PDFs to analytic PDFs

## Slide 13
Barrel DIRC Technical Challenges
Optics
Production of large fused silica bars or plates
Strict mechanical tolerances on shape with optical finish and long sharp edges
Few potential vendors worldwide
High refractive-index lens system
Photon Detection
Single photon detection
Spatial resolution ~ few mm
Fast rise time
Operation in 1 T field
High-rate capability ~0.2 MHz/cm2
long lifetime: 0.5 C/cm2 per year at 106 gain
Fast Frontend
Electronics
High-precision timing
Fast high-bandwidth pre-amplifiers
Radiation hardness
Trigger-less DAQ
Large data volume (up to 200 Gb/s)
Power consumption
Notes: Explain technology challenges using model

## Slide 14
~30 bar and plate prototypes from different vendors
  Different fabrication process and bulk materials
Characterise bar surfaces and shape with lasers
  Bulk transmission
  Internal reflection coefficient
Sensitive to surface roughness and subsurface damage
  RMS roughness (indirect) with 1-2 Å precision
Barrel DIRC Radiator
Notes: Surface properties
Bar geometry

## Slide 15
Photonis Planacon 64ch MCP-PMT is preferred sensor
ALD technique improves lifetime
  6 C/cm2 reached
Meets PANDA requirements
Barrel DIRC Photon Detector
A. Lehmann, Improved Lifetime of MCP-PMT, Tue, 17:40
Notes: MCP-PMTs life time development

## Slide 16
Barrel DIRC Frontend Electronics
MCP-PMT
connector
NINO
PADIWA
Pre-amplifier
Card (16ch)
Discriminator
Card (16ch)
LVDS output+ slow control
Current feedback amplifier (THS3201)
NINO ASIC
(8 ch)
MCP-PMT
connector
Pre-amplifier
(MMIC)
FPGA
(Lattice MachXO2)
LVDS output
FPGA programming interface
Power supply
(+5V)
DAQ system based on TRBv3 board (developed at GSI)
  High-resolution TDC (<10 ps) based on FPGAs
  LVDS input signals
Precise timing
  Amplitude information (ToT)
Compare different technologies
  ASIC: NINO chip (ALICE TOF)
  FPGA: PADIWA (GSI)
Charge (pC)
M. Cardinali, Frontend Electronics for high-precision single photo-electron timing using FPGA-TDCs, Poster
Time-over-Threshold (ns)
Notes: FEE development
TRB system + NINO Frontend card

## Slide 17
Prototypes in test experiments
2009 – GSI
  Proton beam, E~2 GeV
  Oil tank
2011 – CERN T9
  Mixed hadron beam, p<15 GeV/c
  Oil tank
2012 – CERN T9
  Tracking stations
  Time-of-Flight system
  Fused silica prism
  3x3 Planacon MCP-PMT matrix
  896 readout channels
  Bars & plate tested (diff vendors)
Barrel DIRC Prototypes
CERN T9 (2012)
C. Schwarz, Prototyping the PANDA Barrel DIRC, Poster
GSI (2009)
CERN T9 (2011)
Notes: Test beam results from CERN 2012
Pattern with prism attached
Look at Greg’s talk!
896 ch corrspond to ~6% of full system

## Slide 18
2012 Analysis in progress
  3D tracking to be added
  Improve timing/position calibration
  Plate reconstruction in preparation
Preliminary results from bar setup show reasonable agreement with simulation
Barrel DIRC Prototypes
10 GeV/c, 120˚
Number of detected photons
Simulation: Qc=824 mrad, sQc≈9 mrad
Qc=825 mrad
sQc≈ 11 mrad
preliminary
preliminary
Notes: Test beam results from CERN 2012
Pattern with prism attached
Look at Greg’s talk!
Results are from 2012 with InSync bar and spherical lens + 2.2mm air gap

## Slide 19
2013 – MAMI B, 855 MeV electron beam
Test of frontend electronics
  Timing resolution
  Time walk correction
  Thresholds
Barrel DIRC Prototypes
57˚
NINO
PADIWA
w/o correction
Walk correction
Time (ns)
frequency
Notes: MAMI 2013 results
Picture of our prototype
Image
Timing results

## Slide 20
Barrel DIRC is a key component of the PANDA PID system
Challenging R&D program
  Radiator production
  Compact expansion volume
  High refractive-index optics
  Photon detection in strong magnetic field
  Fast frontend electronics
Sophisticated prototypes to verify performance
  Decision on radiator geometry in 2014
TDR ready end of 2014
Installation planned for 2017
Ready for commissioning in 2018
Conclusions
Geant simulation of hit pattern for narrow bars and oil tank geometry

## Slide 21
PANDA Cherenkov Group
FAU Erlangen-Nürnberg
GSI, Darmstadt
HIM, Mainz
JGU Mainz
JINR Dubna
JLU Giessen
Uni Glasgow
Uni Wien
Geant simulation of hit pattern for narrow bars and oil tank geometry