## Slide 1: The ALICE-HMPID performance during the LHC run period 2010-2013
(and perspectives)
G De Cataldo, INFN Bari, It
on behalf of ALICE collaboration
Notes: HMPID acronym stays for high momentum particle identification detector and it is based on RICH counters. It was proposed to ALICE in the 1993 and took its final shape with the TDR in 1998. Finally installed in ALICE on sept 2006. It was the first detector to be installed in ALICE

## Slide 2: ALICE-HMPID
ALICE:
A
Large
Ion
Collider
Experiment
HMPID
ALICE was conceived and built for the study of the de-confined hadronic matter;
Excellent PID capabilities.
A-side view
Notes: A LARGE ION COLLIDER EXPERIMENT to study the deconfined hadron matter and the parton-hadron transition. Its excellent PID relays on ITS TPC TOF TRD and HMPID: location

## Slide 3: Outlines
HMPID presentation,
Detector stability and performance
Introduction to the statistical and track by track PID performances
Perspectives for the HMPID in LHC Run2 (2019-2021)
Summary

## Slide 4: HMPID
High
Momentum
Particle
Identification
Detector
Institutions:
INFN and Dip. Of Physics, Bari (Italy);
Politecnico of Bari (Italy);
CERN Geneva (Switzerland);
Universidad NacionalAutonoma de Mexico, Mexico City(Mexico);
Wigner Research Institute Budapest (Hungary)
~ 20 scientists;
7 RICH modules ~1.3 x1.3 m2 for a total CsI active area of ~11 m2
September 2006: HMPID installation in ALICE magnet!
For the contribution of HMPID to the ALICE physics see D. Di Bari presentation, session Data Analysis and Pattern recognition;
For the pattern recognition role in the HMPID PID please see G. Volpe’s poster in this conference.
Notes: HMPID insertion in the ALICE MAGNET , M0-M6 HMPID layout, services bottom right, C6F14 distribution station, cooling panels, collision points behind the photo plane,

## Slide 5
THE HMPID BASIC ELEMENTS
qc
, qp
Proximity-focusing geometry
Radiator:
15 mm C6F14; n=1.2989 @ 175 nm
Photoelectron detector:
MWPC 2,2-2.5 mm asymmetric gap with CH4 at atmospheric pressure, gas gain  4 104 and analogue pad read-out ( pad size = 8x8.4 mm2,
total channels  160 K
Photon converter:
300 nm thick reflective layer
of CsI; QE  25% @ 7.1 eV (175 nm)
PID range:
1 < p < 3 GeV/c p, K
1.5 < p < 5 GeV/c p

## Slide 6: Detector stability and performance
Photocathode 1
Photocathode 4
Photocathode 3
Photocathode 5
Photocathode 2
Photocathode 0
Back view of the HMPID module and its segmentation
6 CsI pad Photocathodes
6 x HV sector of 48 anodic wires
6 x FEE sectors
2 RO sectors
Dissipated power ~400W /module
Details : CERN/LHCC 98-19 ALICE TDR 1 14 of August 1998
HV5 and FEE5
HV4 and FEE4
HV3 and FEE3
HV2 and FEE 2
HV1 and FEE 1
HV0 and FEE0
ROL
ROR
Notes: To minimize hardware failure the HV, FEE and RO electronics on each module have been segmented; one HV sector covers two pc’s

## Slide 7: Stability of FEE-RO, Cooling and Pw Suppliers
For the FEE and RO electronics, based respectively on the GASSIPLEX and DILOGIC chips, no major problems occurred preventing a regular detector operation;
The FEE dead channels are of the order of 0.15%, no RO board failures have been noticed whereas two Readout Common Board out of fourteen, from time to time have shown loss of connection that in turn could be recovered by a power ON/OFF cycle of the RO electronics;
The cooling system and power supplies have worked stably and according to the expectations;
An effective DCS system has all the time allowed a careful remote detector control monitoring and condition data archiving.

## Slide 8: MWPC HV failing sectors
MWPC 100 mm crimped cathode wires
HV failing sector
M5HV1 : failing 2006
M4HV0 : failing 2009
M0HV3 : failing 2009
M0
M1
M6
M5
M2
M3
M4
Notes: 42 HV sectors. The HV segmentation has prevented that 3 wires switch off three MWPCs; reparation not possible unless detector complete dismounting: serious problem; location of the failing sectors.

## Slide 9: Gas gain monitoring per HV sector
M2HV0 LHC10c data MIP charge distribution
Stability Gas gain value is a critical parameter for the:
single photon detection efficiency e spde
Photon feedback;
CsI ageing by avalance ions.
Actual value ~4 104 (HV=2050 V)
Invers of the slope (changed of sign) gives <spe ph> in ADC channels, the A0 of the Furry distrib. In this case A0 =33 ADC chs.;
s electronic noise = 1 ADC ch ≈ 1000 e-;
cut applied on the bkg: Ath =4 ADC chs.
Actual e sped ≈ 90%
Single electron pulse high distribution
Notes: Rem 573/33 =17 n elettr primari ; 1 ADC = 1000 electrgas gain = 573000/17=≈ 3.3 104

## Slide 10: HV equalization and A0 stability
Trend views of the gas gain stability;
Equalization of 42 HV sectors during LHC11 d-e periods to get A0 ≈ 35;
Gas gain variations vs. time after the equalization ≈ ± 15%
A reduction of 20% for A0 results in a a single photoelectron detection efficiency loss of 3% , no effects on the PID performances, and this thanks to the A0/ Ath ≈ 35/4;
HV equalization
Notes: Time scale extension on the trends depends on the run periods in that year;

## Slide 11: A0 spread per HV sector
(After the HV equalization)
(Before the HV equalization)

## Slide 12: C6F14 circulation system
Excellent stability and easy maintenance thanks to accurate system design;
Safe C6F14 gravity flow;
Separated control of each radiator vessel;
Welded joints;
C6F14 : 3M PF5060DL.
Notes: Detail: Distribution station for one RICH module

## Slide 13: C6F14 transparency monitoring
Two ways of operation for the circulation system: 1) stagnant (OFF) and 2) recirculating with purification (ON);
No evident variation of NČph detected with purification ON or OFF (see later);
In turn observed refractive index variation due to T variation with circulation ON or OFF;
To reduce the C6F14 loss by evaporation and the n variation with T (inhomogeneous data sets!), as from 2013 recirculation OFF during data taking. Purification only during LHC technical stops.
Notes: Cercare convoluzione trasparenza pg 35 convolution

## Slide 14
Angular resolution on q Č
C6F14 Recirculation and purification ON
Data set LHC11e, September 2011
C6F14 Recirculation and purification OFF.
Data set LHC10b, April 2010
C6F14 TOFF >TON No significant variations on q Č resolution, in turn <q Č> is shifted
Notes: TOFF>TON and teta OFF<teta ON < nOFF<nON

## Slide 15
21 quartz-NEOCERAM radiator vessels 1330x 413 mm2 x 15 mm for the 7 modules. All the elements are glued with Araldite 2011;
Left photo: final assembly and layout in the backplane of one RICH module;
right photo: stainless steel inlet fitting (chicane element) glued on the NEOCERAM element of the vessels;
C6F14 inlet fitting (chicane element)
3 radiator vessels 1330x 413 mm2 x 15 mm /module
C6F14 leaks in the radiator vessels

## Slide 16: C6F14 leaks in the quartz radiator vessels
The leaking radiators (white rectangles) were produced during the first period 2002 -2003;
The position of two leaking radiators correspond to the highest hydrostatic pressure values;
No impact on the Q.E. of the other CsI photocathodes;
Combining HV sectors and radiator vessel failures the present HMPID acceptance is 72%;
Statistics still sufficient for inclusive measurements of hadron production;
With stable conditions of the detector no limitations on the measurements are expected during run2;
Notes: Since the HMPID installation (2006) up to now, 4 out of 21 vessels have shown C6F14 leakages; Immediately excluded from the C6F14 recirculation system; Np impact on the CsI Q.E. in affected RICH modules; vessels with the year of production and the date when the leakages manifested (the interaction point is behind the figure plane);

## Slide 17: Preliminary study on the Q.E. stability of CsI photocathodes
A direct measurement of the CsI Q.E. from data is not possible, convolution of several factors;
Monte Carlo procedure for extracting the CsI Q.E. from data and compare with that at the production time of the photocathodes, is under way.
Meanwhile here is proposed an indirect way to check the stability of CsI Q.E. via the number of detected Cherenkov photons NČ.ph;
The results are already normalized to the C6F14 transparency and gas gain;
One out of six pad photocathodes installed in each RICH module;
8x8.4 mm2 pads visible;
CsI not yet evaporated.

## Slide 18: NČ.ph. vs. sin2q and single-photon Č angle resolution
The single-photon Cherenkov angle resolution is extracted for charged p at saturation (p > 1.5 GeV/c);
no cut is applied on the incident track angle.
Number of photon clusters per ring vs. sin^2 Theta_Cherenkov,
The number of photon clusters per ring is extracted from rings fully contained on the photocathode;
Data set: LHC 10b period. B)
Notes: 14 photons for 1 cm radiator in the TDR. Pag 66 hmpid tdr:11.59 mrad 350 GeV/c pions for perpendicular tracks and A0 40 ADC channels. Rem res from geometric (photon emission point), chromatic and localization on photocathode errors

## Slide 19: Stability of detected NČ.ph. at saturated Č angle
Average number of reconstructed photons per track at saturated Č angle per photocathode. The gas gain normalization has been applied. C6F14 transparency: no impact;
to preserve enough statistics, also no fully contained rings are accepted;
Absence of loss trend on NČ.ph., ,confident that no CsI Q.E. loss has taken place;
Notes: acceptance loss on each photocathode
The error bars are the rms of the distribution, for the staistical error on the average it should be divided by sqr(Nev sen2qmax bin)
Rem: caution: different run period/year!

## Slide 20: Spread of detected NČ.ph.
Spread of the average number of photons per photocathode during the run period LHC 13b . Error bars are the r.m.s. of the distributions.
Error bars are the r.m.s. of the distributions

## Slide 21: Cross check of CsI Q.E. stability vs Charge dose
Black curve: total MWPC anode current Ia distribution (in mA) in the six HV sectors of the M0 during 2010-2013;
The double peak: HV rampup during the transitions STANDBY -> BEAM TUNING and BEAM TUNING -> READY;
Red curve: Ia values with HV set at the nominal value: 2050 V.
50nA 200nA
50nA 200nA
50nA 200nA
50nA 200nA
50nA 200nA
50nA 200nA

## Slide 22: Specific charge dose vs. time: the integral of Ia
Integral of Ia in the RICH0. Periods with enhanced slope refers to high luminosity period (pp 2011) or background contaminated period (second half of 2012) or the pPb period (beginnings 2013). A pedestal value of 1 nA has been subtracted to the Ia.
About 72 % of the specific charge dose from pp collisions whereas the 28% from PbPb and pPb. Contributions expected from TDR (1998) were: 4/5 from pp and 1/5 frm PbPb
From p-Pb collisions 2013
2010 2011 2012 2013
2010 2011 2012 2013
2010 2011 2012 2013
2010 2011 2012 2013
2010 2011 2012 2013
2010 2011 2012 2013

## Slide 23: Delivered specific charge dose on CsI photocathode pads
Specific charge dose delivered by the 42 HV sectors on the corresponding photocathodes during the LHC run period 2010-2013; run types pp, p-Pb and Pb-Pb are summed on.
The average value of 0.015 mC/cm2 is well below the threshold of 0.2 mC/cm2 for possible CsI ageing effects. On the base of the LHC scheduled program there exist still safe margin up to 2021!
No CsI ageing effects should be observed up to 2021
The CsI cathode pad current from a conservative model can be assumed as
Icp= f*Ia =0.6 Ia
where
f = (1/2 + Nphotons*r) ;
(1+ Nphotons*r)
<Nphotons>/charged particle = 3
from 2010-2013 data.
r= Ao/<MIP>;

## Slide 24: ALICE-HMPID PID

## Slide 25: HMPID PID performances
PID in pp or pPb collisions
HMPID Cherenkov angle vs track momentum for p-Pb @ 5.02 TeV data;
Low track multiplicity w.r.t. Pb-Pb collisions: negligible background;
The pp PID performances are equivalent to what observed in p-Pb.
Notes: Continuous lines represent theoretical Cherenkov angle values vs. track momentum.

## Slide 26: Collage of p-Pb events
Collage of several low occupancy p-Pb events at SQRT(sNN)= 5.02 TeV 2013 .
Average number of charged particles per event in pp =~ 0.03 for an occupancy of ~ o.o2%

## Slide 27: Statistical PID in pp collisions
Distribution of the Cherenkov angle measured in the HMPID for negative tracks for pp 7 TeV collison. A three-Gaussian fit is applied to evaluate the raw yields.
The separation (n sigma) for p/K and K/p as a function of transverse momentum in HMPID.
HMPID Statistical PID in pp @ 7 TeV sqrt(s), successfully used for measurements of inclusive hadrons production

## Slide 28: Pb-Pb events
PID in Pb-Pb collisions
Event display of Pb-Pb collisions @ SQRT(sNN)=2.76 TeV 2011
Average number of charged particles in Pb-Pb = 50 , for an occupancy of ~3 %
Different background level w.r.t. pp due to high multiplicity environment.

## Slide 29: Statistical PID in PbPb collisions
For raw yields of particle species three-Gaussian fit is applied. “Background” fitted with a sixth order polynomial function;
“Background”: wrong associated angles due to geometrical effects: the larger the Č angle the higher the number of spurious clusters in the sampling band explored by the pattern recognition algorithm.
The algorithm tuning to the event multiplicity in ALICE to reduce the wrong association (contamination), is under way.
Notes: For the raw yield of species a three gaussian fit is carried out . Algorithm tuning already tested and well managed in STAR.

## Slide 30: Track by track PID
As starting estimate of purity and contamination without optimization of wrong associations are extracted from MC for p in PbPb collisions @ 2.76 TeV in 0-5% (left panel) and 40-50% centrality (right panel) intervals .
For the 0-5% centrality bin the relative abundance of p spoils accordingly the p purity. Same calculations available also for p and K; (for details see ‘Charged hadrons identification with the ALICE HMPID at LHC’ of D. Di Bari)
Different centrality bins
Np sigmas <2
Np sigmas <2
Nsigma PID estimator
Physics studies as the elliptic flow, jet and correlations using Track by Track PID with the HMPID, require the knowledge of purity and contamination for each particle species;

## Slide 31: Perspectives for the HMPID in LHC Run2 and beyond up to 2021
After measuring the specific charge dose accumulated during Run1 and extrapolating its computation at the end of Run2 , no Q.E. loss should be observed up to 2018 due to CsI ageing effects;
At the beginning of the Run3 period , the new DAQ schema of ALICE, not limited any longer by TPC event read out rate at 500 Hz, will let to fully exploit the HMPID capability of 2.5 KHz of event rate for central PbPb events up to 2021;
In this perspective the HMPID has already contribute to the ALICE LoI and DAQ-Trigged TDR upgrade documents.

## Slide 32: Summary
Statistical PID in pp successfully carried out for the measurement in ALICE of the inclusive hadron productions ;
With Track by Track PID in Pb-Pb collisions, physics studies with HMPID on the elliptic flow, jet and correlations , are started . An improved pattern recognition algorithm reducing the wrong association of Č angles is being to be put in place;
The Good detector stability during 2010-2013have provide stable PID performances;
72% of HMPID acceptance still active after the HV sector and vessel failures;
Some concerns about further C6F14 leaks in the radiator vessels, in turn no loss of CsI Q.E. in the affected RICH modules ;
No loss of detected NČ.ph observed, good perspectives for the CsI Q.E. up to 2021;
For the HMPID contribution to the ALICE physics please see the D. Di Bari presentation ‘Charged hadrons identification with the ALICE HMPID at LHC’ , in this conference.